## Slide 1: Anomaly Detection in IoT Devices: A Case Study in Predictive Maintenance
Dr. Pooja Sarin
20 Feb, 2025

## Slide 2: Introduction to Anomaly Detection
IoT sensors monitor machinery conditions in manufacturing.
Predictive maintenance reduces downtime and failure costs.
Anomaly detection identifies unusual patterns in sensor data.
Key data sources: Temperature, vibration, and pressure readings.

## Slide 3: Types of Anomalies in IoT Data
Point Anomalies: A single extreme data point (e.g., sudden temperature spike).
Contextual Anomalies: An anomaly based on context (e.g., high vibration at idle time).
Collective Anomalies: A pattern of unusual values over time (e.g., continuous pressure increase).

## Slide 4: Challenges in Time-Series Anomaly Detection
Sensor noise and drift can create false anomalies.
Seasonality and trends make anomalies harder to define.
Concept drift changes normal patterns over time.
Real-time processing requires fast and scalable detection methods.

## Slide 5: Model Performance Interpretation
False Positive Rate (5%): Normal data incorrectly flagged as anomalies.
- Leads to unnecessary maintenance and costs.
False Negative Rate (10%): Actual anomalies missed by the model.
- Can cause undetected failures and damage.
Improvement Strategies:
- Adjust decision thresholds.
- Use ensemble models (Isolation Forest + LSTM).
- Feature engineering to capture meaningful signals.

## Slide 6: Machine Learning Algorithm for Anomaly Detection
Best choice: Long Short-Term Memory (LSTM) Networks
- Handles sequential sensor data effectively.
- Learns long-term dependencies and trends.
- Can be trained in an unsupervised manner using autoencoders.
Alternative Algorithms:
- Isolation Forest (unsupervised)
- One-Class SVM (for small datasets)
- Autoencoders (latent space anomaly detection)

## Slide 7: Conclusion & Next Steps
Anomaly detection in IoT devices helps prevent costly failures.
Challenges include noise, seasonality, and real-time processing.
Balancing false positives and false negatives is crucial.
LSTM is a strong choice for time-series anomaly detection.
Future enhancements:
- Real-time edge computing for instant anomaly alerts.
- Reinforcement learning for optimizing maintenance strategies.